## Slide 1: Composability in the OFMF
Christian Pinto, Michele Gazzetti, Atul Sandur

## Slide 2: OFM Interfaces Diagram
Composability Layer
OFM Services
Hardware Manager(s)
Gen-Z
Agent
Slingshot
Agent
IB
Agent
Application Domain
Fabric Resources
Monitoring
Clients
Resource Inventory
Management Layer
Hardware Layer
Redfish/Native
Translation
CXL
Agent
RESTful API (RF/SF)
Data Store
Composition
Policies
Resource
Control
(e.g., Compute, FAM, Storage, Fabric)
RedFish
Vendor Native API
Administration Domain
Data Store
RF tree management
Infra management
Systems composition
Systems update
App driven system reconfig
Events & Logs
Authentication
Access Control
Events & Logs
Events
Events
Resource Configuration
Fabric Configuration

## Slide 3: Composability Layer
Composability Layer
Fabric Resources
Monitoring
Composition
Policies
Resource
Control
(e.g., Compute, FAM, Storage, Fabric)
Data Store
Main functionalities exposed to clients
Composition/Deletion of Computer Systems
Dynamic update of Computer Systems resources
Application driven dynamic resources configuration and provisioning
  Creation of shared memory region across nodes
  On-demand provisioning of accelerators
  Virtual network creation
  etc.
Management of client permissions/resource ownership
Components
Data store: information on composable resources available, resources bookkeeping, composed/provisioned resources ownership, etc.
Fabric Resources Monitoring: tracks current fabric state and updates local data store based on events.
Composition policies: select resources according to incoming requests constraints and fabric state
Resource control: interacts with OFMF for manipulating RedFish tree to fulfill requests
Events & Logs

## Slide 4
This layer is composing computer systems and updating them at the ResourceBlock (RB) granularity
RBs are the RedFish unit of Composability
RBs are part of the OFMF RF tree and are created by Agents
  Why:
    Only agents have enough information on the fabric for figuring out which components are part of a resource block.
    RBs are the containers of physical resources and are required from initialization time when no ComputerSystems are available
Composability Layer
Fabric Resources
Monitoring
Composition
Policies
Resource
Control
(e.g., Compute, FAM, Storage, Fabric)
Data Store
Events & Logs
Composability Layer

## Slide 5
Data Store: stores the RF tree
  Systems
  Fabrics
  Chassis
  ResourceBlocks for composability
  Any other redfish object needed for representing a complete infrastructure
RedFish Tree management:
  Actions for manipulating the RF tree in response to Client’s requests, including interacting with Agents whenever needed
Events & Logs
  PUB/SUB based service
  Forwarding Agent events to OFM Services and Clients
Authentication and Access Control
  Verify Clients and Agents identity
  Restrict access to resources and services depending on identity
Open Fabric Manager

## Slide 6
Events & Logs:
Retrieves events from Agents
  This could result in changes to the RF tree
Forwards Events from agents to clients
Open Fabric Manager

## Slide 7
RESTful API (RF/SF)
Events and Logs
Fabric Manager Client
RF-FM/FM-RF
translation
Fabric Manager Client
  Interacts with FM via fabric specific APIs
RF-FM/FM-RF translation
  Command, events and objects translation and forwarding from RF to FM schema (and vice versa)
  Expose fabric resources in RF model at initialization time
  Trigger events generation to notify changes in the fabric
  RF objects annotation with fabric related metadata to support composability policies (e.g., resources latency, maximum bandwidth, TBD, etc.)
Events and Logs
  Forward events to OFM
  Logs fabric changes history
Fabric Agent

## Slide 8: Composability Example System Bring UP

## Slide 9: Composability Example System Composition