## Slide 1: Redfish modeling of CXL resources
- Christian, Michele, Atul

## Slide 2: Composable system example: physical resources
Composable module 1
1 CPU Unit
1 DRAM Unit
Composable module 2
1 DRAM Unit
1 CXL Port
Models CXL Type-3 SLD
CXL Switch
2 Ports
Composable Module 1
CXL Switch
Composable Module 2
CPU
DRAM
DRAM
CXL link
CXL link
Notes: 1st assumption: FM is running external to any of the modules and the switch
1st question we have to answer:
How does the FM in charge of the switch recognize what is in module 1 and module 2?
FM on an mC connected to the switch. There is a local agent (BMC) on CM1 that can communicate with the FM. Same on CM2.
In-band, what does the FM know about these modules? (assumption is that there is an agent on CM1 and CM2, not an inband FM. )
OOB, how does the FM know which modules on the OOB fabric are the ones connected to the switch?
Currently, the FM communicating with the agent running on CM1 would not have a way to verify CM1 is connected to the upstream port. Could be a different CM2/3.
In addition, the assumption seems to be for CXL that module 1 and module 2 have a local manager that control the CPU and DRAM mgmt
Yes, we have a Local Manager on CM1/CM2 for this model.
Module 1 must have a local manager to inventory the Non-CXL components if they are to be reported to OFMF or FM.
Module 2 could get by without a local manager communicating to OFMF or FM as long as the DRAM is interfaced to fabric by a CXL device which the FM controls

## Slide 3: Composable system example: composed system
Composable module 1
1 CPU Unit
1 DRAM Unit
Composable module 2
1 DRAM Unit
1 CXL Port
Models CXL Type-3 SLD
CXL Switch
2 Ports
Composed System S1
1 CPU
1 Local DRAM
1 Remote DRAM
Composable Module 1
CXL Switch
Composable Module 2
CPU
DRAM
DRAM
CXL link
CXL link
Composed System S1

## Slide 4: Composable module 1
Chassis
Chassis1
Processors
Memory
CPU1
DIMM1
Ports
1
Root
Systems
CM1
Fabric adapter
Adapter1
MemoryDomains
Domain1
Memory
Chunk
Chunk1
Notes: Assume this is the view of the local manager of CM1...
And that the FM is NOT running on the CM1 host

## Slide 5: Type 3 SLD Memory Composable Module 2
Chassis
Chassis2
Memory
DIMM1
Fabric Adapters
1
Ports
1
Memory Domains
1
Memory Chunks
PCIe Devices
1
PCIe Functions
CXL Logical Devices
1
PCIe Devices
1
PCIe Functions
PCIe Devices
1
1
Chunk1
Should Chunk1 object exist before binding to host is done?
Notes: Assume this is an SLD module in a chassis with a local chassis manager and this is the view the local manager would have.
Chunk1 should not exist before a resource manager creates it, because it is a logical concept, not a hardware one.
This is forward compatible with MLD’s and GFDs.
Don’t configure things before we have to or are asked to.

## Slide 6
Chassis
Chassis2
Memory
DIMM1
Fabric Adapters
1
Ports
1
Memory Domains
1
PCIe Devices
PCIe Functions
CXL Logical Devices
1
PCIe Devices
PCIe Devices
1
1
2
2
Potential extension of Type 3 SLD to Type 3 MLD memory
Memory Chunks
Chunk1
Chunk2
FF
Notes: Same view questions as SLD.
Chunks definitely are not assigned by local manager, because of the required association with an LD, which the FM is responsible for.
If a CXL or Gen-Z memory device doesn’t use DIMMs for volatile memory, Redfish should only have to extend the ‘memory’ definitions or the ‘DIMM’ definitions
If not a DIMM, then Redfish may have to extend the memory object to cover the CXL memory media.
Again, this is the global (OFMF) view
LD ‘FF’ should be shown
Shared memory chunks eventually would have links to more than one LD
Problem: memory chunk AddressRangeOffset is a single property, but for CXL MLD (and GFD?) it is a host-relative value, not an absolute value....
Issue: how does an ‘extent’ (which we want to label as a ‘chunk’) get shared??
How to deal with GFAM?
How to deal with Dynamic Capacity Devices?
Dynamic extents?

## Slide 7: Time T0 : no binding yet, between Composable Module 1 and Composable Module 2
Chassis
Chassis1
Processors
Memory
CPU1
DIMM1
Ports
1
Root
Systems
CM1
Fabric adapter
Adapter1
MemoryDomains
Domain1
Memory
Chunk
Chunk1
Fabrics
CXL
Switches
CXL
Ports
U1
D1
Memory
DIMM1
Fabric Adapters
1
Ports
1
Memory Domains
1
PCIe Devices
PCIe Functions
CXL Logical Devices
1
1
1
Memory Chunks
Chunk1
endpoints
1
2
Notes: First question: is this view that of a global fabric management layer such as OFMF, or is this the host-specific view of the host virtual hierarchy? Yes, this is Global View of OFMF because there is no binding yet.
Since this is before the binding, the host specific view would not have any detail beyond CM1.
Endpoints exist on the fabric as soon as the inventory shows destination or source ports.... IE, its a topology defined entity, not a logical entity
Fundamentally different purpose for PBR-ID vs GCID; PBR_ID is NOT a component ID, and a given component might have more than one PBR_ID.....
LD_ID is not global identifier.
Gen-Z had the GCID.
What does CXL call itself?
Needs a unique instance name which the FM can assign to it. Needs to be globally unique. Needs to be assignable to the device so a new FM can relate the component to the global view.
What is the CXL device ID?
There will be a device SN + vendor device family and version identifier that == UUID eq.
How does the FM know this ID? Can FM alter it? And is it persistent with the device no matter what context the device boots into? IE, does this ID travel with the device, always?
LSA contents are available to host, but how about the FM? (OOB or in-band?)
IF FM is in-band manager, how are MLD’s handled? BIOS would be able to see the FM LD (0xff LD_ID) before FM wakes up. BIOS has to know what NOT to do.
Important NOTE: this Redfish tree implies a solid association between CM1 CPUs, memory, memory domains and a fabric adapter. It also implies a solid association between Chassis 1, a fabric adapter and the memory hosted by the fabric adapter and a PCIe/CXL bus.
There are problems lurking here, however....
The solid associations implied may not be true. If CM1 had two fabric adapters attached, the FM has no way to tell they belong to the same host. Nothing in the CXL spec (that I know of) enables the FM to learn which host is driving a given upstream link of a switch.
The same problem exists on the downstream ports of the leaf switches... Each fabric adapter may be in its own enclosure, as may be any fabric switch. This lack of FRU association is a problem for In-band management. OOB managers may have an advantage per the definition of MCTP addressing hierarchies. Unclear if the upstream ports respond to Switch FM generated MCTP packets.
The FM in charge of a CXL fabric may or may not have access to any kind of description of CM1 beyond the fabric adapter that is attached to a switch which the FM manages.
If the FM is managing components out-of-band, it may have no access to CSRs of the CM1 system’s Fabric Adapter, as CM1 has a local manager. Gen-Z declared how such local managers were to communicate with FM’s; CXL has no such concept. CXL defines how the local BIOS and/or OS reads details out of the hardware devices it finds mapped. In CXL, if the FA is part of the host (IE, the root port), the FM has no ability to manage that logic.
All the same problems arise for a FAM chassis/drawer/appliance.
In general, Gen-Z being in-band managed, had obvious gaps with what the FM can see and manage. CXL, if managed OOB, needs to be explicit about how the FMs can contact or be contacted by the ‘local managers’ of the FRU entities (hosts, FAM drawers, switch enclosures, etc) so that plug and play is possible. In band management meant that FMs and local managers HAD to use a Gen-Z architected mechanism to communicate. CXL is currently in limbo....
Anytime there is a physical link detected and mapped, the question of association with a physical location arises. How does the FM know that FA 1 of CM1 is connected to what is labeled CM1 in the rack?
An interpretation of this view:
This is a global view of the whole installation (IE, the OFMF view)
Each of the major FRUs (CM1, chassis1)

## Slide 8: Time T1 : post-binding between Composable Module 1 and 2
Chassis
Chassis1
Processors
Memory
CPU1
DIMM1
Ports
1
Root
Systems
CM1
Fabric adapter
Adapter1
Memory
Domains
Domain1
Memory
Chunk
Chunk1
Fabrics
CXL
Switches
CXL
Ports
U1
D1
Memory
DIMM1
Fabric Adapters
1
Ports
1
Memory Domains
1
PCIe Devices
PCIe Functions
CXL Logical Devices
1
1
1
CXL
Remote
Endpoints
I1
Connections
1
T1
Memory Chunks
Chunk1
New objects/links

## Slide 9: Backup

## Slide 10: CXL 2.0 memory pooling
Host1
Host2
CXL Switch
Host1
Host2
CXL Switch
FAM 1
FAM 2
FAM 1
FAM 2
Single logical device case
(color coding denotes binding)
Multi logical device case
Host1
CXL Switch
Host1
CXL Switch
Notes: SLD: can have multiple PCIe functions. Can have CXL and Non-CXL functions.
MLD: upto 16 hosts.
FM: initial config to determine devices out there, produce bindings so when host boots, can find the devices, also does allocation/re-allocation of memory dynamically. Also unbinding/re-binding within MLD.

## Slide 11: Type 3 SLD Memory Composable Module 2
Chassis
Chassis2
Memory
DIMM1
Fabric Adapters
1
Ports
1
Memory Domains
1
Memory Chunks
1
PCIe Devices
1
PCIe Functions
CXL Logical Devices
1
PCIe Devices
1
PCIe Functions
PCIe Devices
1
1

## Slide 12: Type 3 MLD Memory
Chassis
Chassis2
Memory
DIMM1
Fabric Adapters
1
Ports
1
Memory Domains
1
Memory Chunks
1
PCIe Devices
PCIe Functions
CXL Logical Devices
1
PCIe Devices
PCIe Devices
1
1
2
2
2